## Slide 1: Engineering Metrology
Tolerances & Allowances

## Slide 2: Accuracy and Precision

## Slide 3: Metrology standards
Sensitivity or resolution is the smallest dimension that can be read on an instrument
Standard measurement should do at the temperature 20  0.3oC
Measuring instruments must have the tolerance more than the desired tolerance for a product 10 times.
  For example, if we want to measure a product with tolerance equal to 0.01 , the instrument that we use must have the tolerance equal to 0.001

## Slide 4: allowance
For assembly parts
The allowance that desire for the different of two or more mating parts
If it is positive,  minimum clearance
If it is negative  maximum interference
Notes: The different between the min diameter of the exterior fitting part (+) and the maximum diameter of the interior fitting part (-)

## Slide 5: Basic size, deviation, and tolerance on a shaft, according to the ISO system

## Slide 6: Fit system (ISO)
Hole-basis system
  Tolerance is at the zero line of hole
  MMC: The basic size is at the smallest hole
Shaft-basis system
  Tolerance is at the zero line of shaft
  MMC: The basic size is at the biggest shaft.
Notes: Because the dimensions of holes are more difficult to control than those of shafts, the hole-basis system is commonly used for specifying tolerances in shaft and hole assemblies.

## Slide 7: Fit between mating parts
Clearance
  One part is always loose relative to the other one.
  Two mating parts have clearance  0
Transition
  Both clearance and interferance
Interference
  One part is always forced tight with respect to another.
  Two mating parts have clearance  0
Notes: ANSI class
clearance class 1-loose, 2-free, and 3-medium
transition class 4-snug, and 5-wringing
interference class 6-tight, 7-medium force, and 8-heavy force
Clearance fit occurs when two toleranced mating parts will always leave a space or clearance when assembled.
Interference fit occurs when two toleranced mating parts will always interfere when assembled. It wold be necessary to stretch the hole or shrink the shaft or to use force to press the shaft into the hole.
Transition fit occurs when two toleranced mating parts are sometimes an interference fit and sometimes a clearance fit when assembles.

## Slide 8: Hole basis system

## Slide 9: Shaft-basis system

## Slide 10: How to calculate allowance
  Maximum clearance = max hole – min shaft
  Minimum clearance = min hole – max shaft
  Maximum interference = max hole – min shaft
  Minimum interference = min hole – max shaft
  Look up from the allowance table
Notes: Max interferance > min interferance  because of the minus value
If they are absolute value, I max interferance l < l min interferance l

## Slide 11
ISO Symbol |  | Description
Hole Basis | Shaft Basis | 
H11/c11 | C11/h11 | Loose running fit for wide commercial tolerances or allowances on external members
H9/d9 | D9/h9 | Free running fit not for use where accuracy is essential, but good for large temperature variations, high running speeds, or heavy journal pressures.
H8/f7 | F8/h7 | Close running fit for running on accurate machines and for accurate location at moderate speeds and journal pressures.
H7/g6 | G7/h6 | Sliding fit not intended to run freely, but to move and turn freely and locate accurately.
H7/h6 | H7/h6 | Locational clearance fit provides snug fit for locating stationary parts; but can be freely assembled and disassembled.
H7/k6 | K7/h6 | Locational transition fit (accurate) for accurate location, a compromise between clearance and interference.
H7/n6 | N7/h6 | Locational transition fit (more accurate) for more accurate location where greater interference is permissible.
H7/p6 | P7/h6 | Locational interference fit for parts requiring rigidity and alignment with prime accuracy of location but without special bore pressure requirements.
H7/s6 | S7/h6 | Medium drive fit for ordinary steel parts or shrink fits on light sections, the tightest fit usable with cast iron.
H7/u6 | U7/h6 | Force fit suitable for parts which can be highly stressed or for shrink fits where the heavy pressing forces required are impractical
Clearance fits
Transition
fits
Interference
fits

## Slide 12: Example
We want to assemble shaft and gear together. The nominal size of both part is equal to 5 mm. Using medium drive fit.
Hole H7 | Shaft s6 | Fit
5.012 5.000 | 5.027 5.019 | -0.007 -0.027
Chose hole-basis system: H7/s6 and basic size = 5 mm. From the table,
The diameter of
the biggest hole = 5.012 mm
the smallest hole = 5.000 mm
the biggest shaft = 5.027 mm
the smallest shaft = 5.019 mm
Minimum allowance = -0.027
Maximum allowance = -0.007