## Slide 1
Grinding is a process which utilizes the use of abrasive particles bounded together to produce superior surface finishing
An abrasive: is a small, nonmetallic hard particle having sharp edges and an irregular shape
Grinding

## Slide 3: Types of Abrasives
Conventional
  Aluminum oxide
  Silicon carbide
Super abrasives
  Cubic boron nitride
  diamond
Notes: The kind of abrasive used depends on the hardness of both the material and the abrasive and also the kind of surface finishing needed

## Slide 4: Grinder Forms cont’d

## Slide 5: Grinder Wheels

## Slide 6: Grinding Wheels
Operations done to preserve the properties of the wheel
  Dressing
  Truing
  shaping
Notes: Dressing: is used when the wheel becomes dull from developing wear flats or when the porosities on the wheel become filled with clogged chips. The process involves removing the external layer of the wheel and exposing fresh cutting abrasive edges to the work piece.
Truing: is a kind of dressing operation where the purpose is to restore the circular shape to the grinding wheel.
Shaping: grinding wheels can be shaped to take the negative of the shape that need to be grinded.

## Slide 8: Dressing

## Slide 9: Grinding Operations
Examples of grinding operations
  Surface grinding
  Cylindrical grinding
  Internal grinding
Notes: Surface grinding: is the process of grinding flat surfaces. The work-piece is mounted on a magnetic chuck or any other clamped device and the wheel is mounted on a horizontal spindle. The table reciprocates vertically and feeds horizontally to allow grinding the whole surface.
Cylindrical grinding: circular cross sections are ground by rotating the work-piece between two centers and moving it laterally on the grinder. Thread grinding also take place on cylindrical grinders.
Internal grinding: small wheels are used to grind the inside of the work-piece.

## Slide 10: Grinding Machines

## Slide 11: Grinding Machines

## Slide 12: Grinding Machines

## Slide 15: Surface Finishing
Any of different processes employed for surface, edge, and corner preparation, as well as cleaning, and coating.
Notes: Surface Finishing usually constitutes a final operation in machining.

## Slide 16: Lapping
Finishing operation in which a loose, fine-grain abrasive in a liquid medium abrades material.

## Slide 17: Lapping cont’d
Lapping is an extremely accurate process
It corrects minor shape imperfections.
Refines surface finishes
Provides a close fit between mating surfaces.
Dimensional Tolerances = 0.00005mm

## Slide 18: Polishing
An operation to smooth off roughness from a work-piece, or put a high finish on metal by using a polishing wheel.
Polishing wheel is a wheel made of one of several kinds of materials and coated with abrasive grain and glue.

## Slide 19: Polishing cont’d

## Slide 20: Questions